## Slide 1: Little endian
BYTE 0 | BYTE 1 | BYTE 2 | BYTE 3
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Signal 1
Length : 4 bits
Max Val : 15 decimal
Start bit : 0
Byte : 0
Stop bit : 3
Signal 2
Length : 5 bits
Max Val : 31 decimal
Start bit : 0
Byte : 1
Stop bit : 4
Signal 3
Length : 2 bits
Max Val : 3 decimal
Start bit : 0
Byte : 2
Stop bit : 1
Signal 4
Length : 6 bits
Max Val : 63 decimal
Start bit : 0
Byte : 3
Stop bit : 5
Signal 2 Val : 29 decimal
Signal 1 Val : 11 decimal
Signal 3 Val : 2 decimal
Signal 4 Val : 61 decimal
0x0B | 0x1D | 0x02 | 0x3D
Values sent on the network BYTE 0 BYTE 1 BYTE 2 BYTE 3
When signal 1 , signal 2 and signal 3 and signal 4 is fed with 11, 29, 2 and 61 values below is the data which reflects on network when it is converted into LITTLE ENDIAN

## Slide 2: Big endian
BYTE 0 | BYTE 1 | BYTE 2 | BYTE 3
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Signal 1
Length : 4 bits
Max Val : 15 decimal
Start bit : 4
Byte : 0
Stop bit : 7
Signal 2
Length : 5 bits
Max Val : 31 decimal
Start bit : 3
Byte : 1
Stop bit : 7
Signal 3
Length : 2 bits
Max Val : 3 decimal
Start bit : 6
Byte : 2
Stop bit : 7
Signal 4
Length : 6 bits
Max Val : 63 decimal
Start bit : 2
Byte : 3
Stop bit : 7
Signal 2 Val : 29 decimal
Signal 1 Val : 11 decimal
Signal 3 Val : 2 decimal
Signal 4 Val : 61 decimal
0xB0 | 0xE8 | 0x80 | 0xF4
Values sent on the network BYTE 0 BYTE 1 BYTE 2 BYTE 3
When signal 1 , signal 2 and signal 3 and signal 4 is fed with 11, 29, 2 and 61 values below is the data which reflects on network when it is converted into BIG ENDIAN
3 | 2 | 1 | 0 |  |  |  | 
4 | 3 | 2 | 1 | 0 |  |  | 
1 | 0 |  |  |  |  |  | 
5 | 4 | 3 | 2 | 1 | 0 |  | 
Above blue slots indicate network bytes and green bytes indicate signal data, signals 0th bit sits in networks 4th bit in first signal, in second signals 0th sits in networks 3rd bit.

## Slide 3: Big endian -2
BYTE 0 | BYTE 1 | BYTE 2 | BYTE 3
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Signal 1
Length : 14 bits
Max Val : 16383 decimal
Start Bit : 2
Start Byte : 1
Stop Bit : 7
Stop Byte : 0
Signal 2
Length : 15 bits
Max Val : 32767 decimal
Start Bit : 3
Start Byte : 3
Stop Bit : 1
Stop Byte : 1
Signal 2 Val : 32757 decimal
Signal 1 Val : 13285 decimal
0xCF | 0x97 | 0xFF | 0xA8
Values sent on network BYTE 0 BYTE 1 BYTE 2 BYTE 3
D | C | B | A | 9 | 8 | 7 | 6
5 | 4 | 3 | 2 | 1 | 0 |  | 
Above green slots indicate network bytes and blue bytes indicate signal data, first signals 0th bit sits in 2nd bit of network byte 1 and signals last bit sits on 7th of ntks 1st byte
 |  |  |  |  |  | E | D
C | B | A | 9 | 8 | 7 | 6 | 5
4 | 3 | 2 | 1 | 0 |  |  | 
 ---------------------------- Signal 1 ------------------------ 
 ---------------------------- Signal 2 ------------------------------- 

## Slide 4: Little endian -2
BYTE 0 | BYTE 1 | BYTE 2 | BYTE 3
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Signal 2 Val : 2000 decimal
Signal 1 Val : 262140 decimal
0xFC | 0xFF | 0x43 | 0x1F
Values sent on the network BYTE 0 BYTE 1 BYTE 2 BYTE 3
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
F | E | D | C | B | A | 9 | 8
 |  |  |  |  |  | 1 | 0
5 | 4 | 3 | 2 | 1 | 0 |  | 
 |  |  | A | 9 | 8 | 7 | 6
Below is signal 1 where it starts from 0th bit of byte 0 and later starts from 0th bit of byte 1 and later starts from 0th bit of byte 2
Below is signal 2 where it starts from 2nd bit of byte 2 and ends at 4th bit of byte 3
Signal 1 is of 18 bits length , it write from 0th bit of 0th byte and again starts from 0th bit of byte 1 and again from 0th bit of byte 2 since it has 18bit length it ends at 1st bit of byte 2, we are sending decimal value of 262140 on network.
Signal 2 is of 11bit length it starts from 2nd bit of byte 2 and ends at 4th bit of byte 3, we are sending value 2000 on the network which is in decimal
When we write signal 1 value 262140 on network byte in little endian and for signal 2 , 2000 in little endian on network byte.
It would be sent as 0xFC, 0xFF, 0x43 and 0x1F